## Slide 1
Architettura Layer 2
INNOVAZIONE NELLE RETI DI ACCESSO
A BANDA ULTRALARGA
e nuove sfide operative
Franco Grisolia
Eurekalabria 2026 | 24 settembre 2026

## Slide 2
The evolution of the FWA offering
LAYER 2 IS THE OUTCOME OF A BROADER EVOLUTION ACROSS NETWORK, SYSTEMS AND THE WHOLESALE OFFERING
EXANDED
NETWORK REACH
WINDTRE TECHNOLOGY AND SYSTEMS INTEGRATION
FWA LAYER L3
FWA LAYER L2
Extended network coverage and mobile access for wholesale services.
Integration into the Group’s technology and operational architecture.
Launch of the wholesale FWA Layer 3 offering, with IP-level service delivery.
A new Layer 2 access model providing operators with greater control, flexibility and network integration.
2025
2026
YE26
FOUNDATIONAL ENABLERS
FWA OFFERING EVOLUTION

## Slide 3
Architectural Technical Choice
OVN: OVERLAY VIRTUAL NETWORKING
Layer 2 transport of traffic aggregated over the FWA access is enabled through a VxLAN tunnel established between the Outdoor Unit (ODU), supplied by OPNET, and the HUB node connected to the wholesale customer.
Based on the number of user VLANs configured at the customer site, each of the two tunnel endpoints
(VTEPs, VxLAN Tunnel EndPoint) may be associated with one to three VNIs.
The solution is highly scalable, allows to manage up to 16 million VLANs.

## Slide 4
Challenges faced
IT'S "ONLY" AN ODU
ODU New Feature VxLAN
QoS
New
VLAN
TAG
Easy
config
New Chipset
4

## Slide 5
MAC Header
IP Header
UDP Header
VXLAN Header
Original Layer 2 Frame
FCS
Destination MAC
Source MAC
VLAN Type
VLAN ID TAG
EtherType
IP Heasr Misc Data
Protocol 0x11
Header Checksum
Outer Source IP
Outer Destination IP
UDP source port
VXLAN Destination Port
UDP Length
UDP Checksum
VXLAN Flags
Reserved
VNID
Reserved
MAC | IP | TCP/UDP | Payload
18 Bytes
20 Bytes
8 Bytes
8 Bytes
54 Bytes of Overhead (realistic)
Challenges faced
VXLAN (VIRTUAL EXTENSIBLE LAN, RFC 7348)
1500 Bytes

## Slide 6
Challenges faced
VTEP
on ODU
VTEP
on E-NNI
VxLAN Tunnel
MTU
MTU
Mobile BackHauling
BB IP
CORE Mobile
RAN (Radio Access Network)
WHOLESALER
FWA
e/g Node-B
SecGW
S-GW
P-GW
E-NNI
USER
IDU
ODU
MTU
MTU
6
MTU
MTU
MTU
MTU
MTU
VTEP
VTEP

## Slide 7
MTU GROWS
Challenges faced
TESTING MTU
1574 byte
1546 byte
1646 byte
MTU
MTU
IDU
ODU
USER
MTU
Data Payload 1546 byte
Don't Fragment
1646
1574
1546

## Slide 8
Use cases
ODU
IDU
VLAN 835
(0,1,5)
Mono VLAN Multi Cos 0,1,5
S-Vlan/C-Vlan
Option #1
Multi VLAN Mono Cos [0]-[1]-[5]
VLAN 835 [0]
ODU
IDU
VLAN 935 [1]
VLAN 837 [5]
3x(S-Vlan/C-Vlan)
Option #2
UNTAG
ODU
IDU
Mono VLAN
UnTAG
S-Vlan/C-Vlan
Option #3
9

## Slide 9
Conclusions
KEY TAKEAWAYS FOR FWA L2 WHOLESALE
10
InDoor Unit (IDU) provided and managed by the Wholesale Customer; caratteristics:
"IEEE 802.1q" and "IEEE 802.1p" standards Maximum MTU 1574 Bytes (at IP level) End-user services provided by the Wholesale Customer (IP address, Voice service,...)
OuDoor unit (ODU) termination of L2 Tunnel provided and managed by OPNET
  FWA Access traffic uniquely identified via an S-VLAN/C-VLAN pair
  An external tag (S-VLAN) An internal tag (C-VLAN) that identifies the FWA Wholesale access of a specific property unit
  Traffic delivered via E-NNI interconnection
  IEEE 802.1q (vlan tagging), IEEE 802.1ad (QinQ), 802.3ad (LACP) MTU set to 9000 Bytes POP available RM Tor Cervara W3 and MI Ortles W3; RM NAMEX and MI Caldera will be added soon
  3 Service Scenarios currently envisaged:
  MONO-COS tagged= up to 3 user VLANs (User-VLAN 835, 837 and 935) with different COS (0, 1 or 5 respectively) MULTI-COS tagged= a unique uvlan (User-VLAN 835) multicolor (COS 0, 1, 5) MONO-COS Untagged= a single untagged VLAN (best effort)

## Slide 10
FWA L2 Architecture

## Slide 11
Thank you
OpNet S.r.l.
Sede Legale Via Monte Rosa 91, 20149 Milano (MI))
www.opnet.it